## Slide 1: Exploiting idle resources in a high-radix switch for supplemental storage
Matthias Blumrich, Ted Jiang, and Larry Dennison November 13, 2018
Notes: Today I will present our paper titled Exploiting Idle Resources in a High-Radix Switch for Supplemental Storage. This is work I did together with Ted Jiang and Larry Dennison.

## Slide 2: Supplemental Storage
Why is it useful?
To enable capabilities in the network: end-to-end retransmission, congestion control, order enforcement, in-network collectives, deadlock recovery, etc.
Where can it be found?
Existing, unused buffer memory
How can it be accessed?
Existing excess internal switch bandwidth
Notes: I want to start with the why, where, and how of supplemental storage. First of all, why is it useful? Well, to enable capabilities in the network such as … Where can supplemental storage be found? Today I’m going to show you how to access existing, unused buffer memory, so I’m not talking about adding more memory to switches. How can we access that unused buffer memory? I’m going to show you how we exploit existing excess internal switch bandwidth.

## Slide 3: Why?
End-to-End Retransmission
Store copies of packets in the first-hop switch until they are acknowledged
Delete when acknowledged (common case) or retransmit if lost
Supplemental storage usage pattern: store, then delete
Great for network reliability! But other uses too.
Explicit Congestion Notification (ECN) enhancement
When network congestion is detected, send throttling commands back to problem senders
Our idea: temporarily store congestion-causing packets to allow others to proceed
Supplemental storage usage pattern: store and retrieve
Notes: To explore the why I’m going to use two examples in this talk, and these are the two we studied in the paper. First, end-to-end retransmission. The idea is to store copies of packets in the supplemental storage of the first-hop switch until they successfully cross the network and are acknowledged. In the common case, the packets arrive successfully and the copies are simply deleted. In the rare case that something goes wrong or a packet is dropped, the copy can be retransmitted. So the supplemental storage usage pattern is primarily store packets and delete them later. End-to-end retransmission is obviously great for network reliability, but there are other uses too. For example, simplifying complex protocols.
The other use case we studied is an enhancement to Explicit Congestion Notification. The basic idea is that when network congestion is detected at the last-hop switch, the protocol sends throttling requests back to the senders that are causing the congestion. But this takes some time to have an effect, so our idea is to temporarily store the congestion-causing packets in the supplemental storage of the congested switch to allow other packets to proceed. In other words, relieve the head-of-line blocking. So the supplemental storage pattern is to store packets and later retrieve them.

## Slide 4: Where?
Buffers are sized for “bandwidth X roundtrip-time” of the longest link
Switch A Port
Output
Retransmission
Buffer
Input
Cut-Through
Buffer
Link
Switch B Port
Output
Retransmission
Buffer
Input
Cut-Through
Buffer
Short
Short links only use a small amount of buffering because storage is relative to actual link RTT
Unused!
Unused!
Unused!
Unused!
Notes: Where does the supplemental storage come from? Consider a typical high-performance link between the ports of two switches. There is a significant amount of buffering in the ports in order to keep the link running at full bandwidth reliably. On the output side, there is a link-level retransmission buffer that holds copies of every packet sent on the link until they are acknowledged by the receive side. Therefore the size of the retransmission buffer is roughly the link bandwidth times the roundtrip-time of the link, or the bandwidth-delay product. On the receive side, there is usually also a large buffer that is used to implement cut-through flow control. When using credit-based flow control this buffer works almost like a mirror of the retransmission buffer. Credits are handed out to grant buffer space to the sender, and new credits are only handed out when data leaves the buffer. Therefore, there is another roundtrip delay between credits going out and corresponding packets coming in, and the size of the buffer is also roughly the bandwidth times the roundtrip time. In a general-purpose switch with symmetric ports, all of these buffers have to be sized for the worst case, or the longest link that can ever be connected to them.
But when a short link is connected, only a small fraction of the buffer space is needed because it is proportional to the actual roundtrip time on the link. Therefore, most of the buffer memory is unused and that is what we use for supplemental storage. In fact, I will show you later that 72% of the port memory is unused in a large dragonfly network.

## Slide 5: How?
Exploit excess internal bandwidth on existing
port-to-port datapaths
We studied a tiled switch
Regular architecture that scales to many ports
Provides any input-to-output permutation
Other switch architectures should work too
Notes: So how do we access the unused port memory. In short, we exploit the excess internal bandwidth on the existing datapaths in the switch. We studied tiled switches, which are an excellent choice for scalability. This cartoon shows how a tiled switch implements a crossbar from the inputs on the left to the outputs on the bottom. The crossbar is divided into several tiles, each of which has a much smaller crossbar internally. The tiled switch provides any permutation of inputs to outputs, so there is a lot of excess capacity. In fact only about 25% of the internal bandwidth is used at any time. We are going to use some of that bandwidth to allow any port to access the supplemental storage of any other port. I should point out that we studied the tiled switch, but we think that other switch architectures that support full permutations should work too.

## Slide 6: stashing
Every port donates its unused memory to a common pool of supplemental storage
Any port that needs additional storage can read/write the common pool
Example: ports connected to endpoints storing packets for end-to-end retransmission
Example: congested ports diverting packets until ECN kicks in
Notes: Our technique for utilizing the supplemental storage is called stashing. The basic idea is that every port donates its unused memory to a common pool of supplemental storage. Then any port that needs additional storage can access the common pool. For example, with end-to-end retransmission, only the ports connected to endpoints need to stash copies of packets. And to help ECN, only congested ports need to divert packets until the algorithm kicks in.

## Slide 7: architecture
Notes: Ok, architecture.

## Slide 8: Baseline Tiled switch
Each input drives a single, multi-drop row bus
Each tile drives point-to-point column buses to outputs
row buses
column buses
Packets proceed in stages between buffers
Stashing takes advantage of the extra bandwidth due to row bus multicast and many column buses
Notes: This is a more detailed picture of the tiled switch showing more buffering. Each input drives a single, multi-drop row bus that spans all the columns. Note that because it’s a bus, it’s possible to write the same packet to more than one row buffer at a time. From the tiles to the outputs, a bus is not possible so each tile drives individual point-to-point column buses to every output in its column. So each output is driven by multiple column buses, equal to the number of rows. I highlighted the path of a packet from input 3 to output 6 in red. The packet proceeds in stages, but the internal buffers are much smaller than the port buffers because they have credit loops based on the short internal datapaths. Stashing takes advantage of the extra bandwidth due to the row bus multicast and the many column buses.

## Slide 9: Baseline switch datapath
Large port buffers (3 virtual channels)
Small internal VC buffers
Crossbar to interleave all inputs of a row to all outputs of a column
Notes: Here’s another view of the datapath through a tiled switch, including the buffers I described. On the left are the large port buffers, sized for the longest possible links. Note that I show 3 virtual channels just as an example. Next, there are the small internal buffers used to stage the packets through the switch. Finally, there is the tile crossbar to interleave all inputs of a row to all outputs of a column.

## Slide 10: Stashing switch datapath
Port buffer memory is virtually partitioned and unused portions are combined for stashing storage
Two internal VCs are added for
storage (S) and retrieval (R)
Extra read and write datapaths are added to the port memories
Notes: Here is our stashing switch, with additional hardware or significant modifications shaded. I changed the way the port buffering is drawn a little to help you understand where the stashing memory comes from. In this picture, you can see that the cut-through and retransmission buffers are a lot smaller because I’m assuming that a short link is connected. Both port buffer memories are virtually partitioned and the unused portions are combined for stashing storage. Next, we add read and write datapaths to the port memories so that the stashing partitions can be accessed without interfering with the normal port activities. Finally, we add two internal VCs: one for storing packets to stashing memory and one for retrieving packets from the stashing memory. The extra VCs ensure that the switch remains deadlock free.

## Slide 11: Storing end-to-end packets
Copy for stashing is written together with the normal VC (multicast)
Note: storage and normal VC can be in the same column (tile) or different
Notes: To make things more clear, I’m going to walk through the two use cases I introduced earlier. First, storing packets for end-to-end retransmission. In the following diagrams, I’ll be showing two different ports so I’ve stubbed off the connections between the input and output side of each port.
A packet comes into the switch and is stored in the cut-through buffer. Eventually it’s broadcast on the row bus across all columns of tiles. Now remember that for end-to-end retransmission, a copy of every request packet has to be made and saved while the normal packet goes on its way. We take advantage of the row bus to do a 2-way multicast of these packets to a normal VC buffer and a stashing storage VC buffer. Here I show these two VC buffers in the same column, but they can be in different columns as well.

## Slide 12: Storing end-to-end packets
Stashing copy requires its own column bus transfer
Notes: Now I’m going to follow only the stashing copy. It competes like any other packet for the tile crossbar and access to a column bus. Once granted, it is transferred to a column buffer.

## Slide 13: Storing end-to-end packets
End-to-end summary:
No additional row bandwidth
because of multicast
Double the column bandwidth
because stashing can be at any port
Notes: Finally, it competes with stashing copies from other rows for access to the stashing partition and gets stored.
So to summarize end-to-end stashing storage, we don’t need any additional row bandwidth because of the 2-way multicast of the row bus. But there’s double the column bandwidth since the stashing copy and the normal transfer happen separately.

## Slide 14: Storing ECN packets
Only stashing VC used (no copy)
Packets are diverted to any port that has stashing space
Notes: The other example is diverting packets in support of the ECN protocol. Remember that the idea is to send congestion-causing packets to stashing storage temporarily to relieve HoL blocking and then allow them to continue on their way. I should mention that we assume a completely unordered network for this study.
Here I show the entire storage datapath. It’s identical to what I showed for end-to-end retransmission except that there is no need to do the 2-way multicast on the row bus since there is no copy made; the packet is simply routed to a stashing buffer on some port.
Therefore, the storage action uses the same amount of bandwidth as the normal send would have.

## Slide 15: retrieving ECN packets
Packets are returned to their original routes
ECN summary:
Two full switch traversals
doubles the row and column
bandwidth
But only for stashing traffic
Notes: Later, the stashed packets have to continue on their way. So they compete for the row bus and then continue on the normal path.
To summarize ECN, diverting packets requires two full switch traversals so it doubles the row and column bandwidth, but only for the stashed packets. Arguably, a congested switch may have excess idle bandwidth, allowing some of the additional cost to be hidden.

## Slide 16: experiments
Notes: On to the experiments. I should be clear that the intention of our study was to determine if this idea has merit, not to work out all the details.

## Slide 17: Dragonfly network
Scalable and cost-efficient topology due to a high degree of link sharing
Network consists of fully-connected groups of fully-connected switches
Group
Notes: We based our study on a dragonfly network which we like for all kinds of reasons. We believe it is a great topology for a scalable and cost-efficient network due to a high degree of link sharing. The canonical dragonfly consists of fully-connected groups of fully-connected switches. Here I show a group with 5 switches, each connected to two endpoints, which are the black squares. The switches are also connected to one another and then each one has connections to switches in other groups. In this case there are ten of the global links in red, so the entire dragonfly consists of 11 groups, shown on the right.

## Slide 18: Dragonfly stashing
Like most large-scale topologies, the dragonfly has asymmetric link lengths
On a general-purpose switch, buffers sized for the long links
72% of all port buffer memory is unused and available for stashing
Because 75% of the ports are connected to short links
Link Type | Length | Ports per Switch | Port Buffers Unused
Endpoint | Very Short (< 1m) | 25 % | 99 %
Within group | Short (< 5m) | 50 % | 95 %
Between groups | Long (up to 100m) | 25 % | None
Notes: Like most large-scale topologies, the dragonfly has asymmetric link lengths and the asymmetry is significant. This chart shows link lengths you might expect for a large supercomputer, where groups consist of a small number of cabinets and the whole machine consists of 100 cabinets or more. So 75% of the links are connected to endpoints and within groups, and they are short. The remaining 25% are connected across the machine and are long. Since a general-purpose switch has port buffers sized for the longest links, 75% of the ports have most of their buffers unused. In fact, if you do the math, 72% of all port buffer memory is available for stashing.

## Slide 19: Experimental method
Simulated a 3080-node dragonfly network using 20-port switches
Each switch is a 4x4 array of 5x5 tiles, with 30% internal clock speedup
Used SST/Macro (system) together with Booksim (switches) to simulate:
Synthetic uniform-random traffic
Six MPI application traces: BIGFFT, AMG, MultiGrid, Fill Boundary, AMR, and MiniFE
Notes: We simulated a 3080-node canonical dragonfly built with 20-port switches, so there were 5 endpoints per switch. Each switch is a 4x4 array of 5x5 tiles. We simulated a 30% internal clock speedup, which is not unusual. We used the SST/Macro simulator for the system and applications, and bookism for the switches and network. We used one synthetic traffic pattern – uniform random – and six MPI application traces.

## Slide 20: End-to-end retransmission
Modeled stashing of packets when sent, and deletion of stashed copies when acknowledged
Did not model actual retransmissions because they are rare and not time-critical
Goal: make sure the common store/delete operations “do no harm”
Goal: determine whether there is sensitivity to the total amount of stashing storage
Compared four models:
Baseline tiled switch
Stashing switch
Stashing switch with only 50% of the stashing buffers available
Stashing switch with only 25% of the stashing buffers available
Notes: I’ll begin with end-to-end retransmission. Again, we modeled the stashing of packets when sent, and the deletion of stashed copies when acknowledged. But we did not model retrieval or retransmission. The first goal of the experiments was to make sure that the frequent store and delete operations did no harm. The second goal was to get some idea of the sensitivity to the total amount of stashing storage. Therefore, we compared four switch models: the baseline tiled switch, the stashing switch, and then a stashing switch with only half of the stashing storage available, and a stashing switch with only a quarter of the stashing storage available.
Note that when the stashing storage is exhausted, the switch inputs back up because their input buffers fill while waiting for a place to stash packets. We did not allow a normal packet to be sent unless it was simultaneously stashed. Backing up inputs like this is bad for performance, but cannot lead to deadlock since the stashing buffers always eventually clear.

## Slide 21: End-to-end retransmission
Stashing primarily does no harm across applications
Sometimes stashing improves the runtime (probably by reducing congestion)
Application runtime normalized to the baseline tiled switch
Chart: Normalized Runtime
| BIGFFT | FillBoundary | AMR | MiniFE | MulitGrid | AMG
Baseline | 1 | 1 | 1 | 1 | 1 | 1
Stash 100% Cap. | 1.0338 | 0.97271 | 1.0017 | 0.99887 | 0.99303 | 0.99967
Notes: Here we compare the baseline switch in red to the stashing switch in green using the six MPI application traces. The chart shows runtime normalized to the baseline switch, so higher is worse. The two traces on the left, BigFFT and FillBoundary send the most data. Overall, you can see that stashing does no harm, except for BIGFFT where is does slightly worse. Curiously, stashing actually improves performance for two apps: FillBoundary and MultiGrid. We suspect that this is due to a natural throttling effect that reduces congestion and is beneficial, but we did not get to the root cause.

## Slide 22: End-to-end retransmission sensitivity
Apps that send the most data slow down when stashing memory is exhausted
Added switches with reduced stashing capacity
Chart: Normalized Runtime
| BIGFFT | FillBoundary | AMR | MiniFE | MulitGrid | AMG
Baseline | 1 | 1 | 1 | 1 | 1 | 1
Stash 100% Cap. | 1.0338 | 0.97271 | 1.0017 | 0.99887 | 0.99303 | 0.99967
Stash 50% Cap. | 1.0319 | 1.018 | 1.0061 | 0.99887 | 0.99303 | 0.98985
Stash 25% Cap. | 1.2966 | 1.086 | 1.0061 | 1.0061 | 0.99303 | 1.0085
Notes: Here I show the same data in the red and green bars, and I add the other two switch models with reduced stashing buffer capacity. The switch with the least stashing storage, in yellow, loses a noticeable amount of performance for the two applications with the highest bandwidth requirement showing that the amount of stashing storage matters. But otherwise, it does about as well as the others. The stashing switch with half the buffer capacity shows little sensitivity. Overall, we conclude that the stashing switch does no harm and is not particularly sensitive to the amount of stashing buffer capacity for the dragonfly we studied.

## Slide 23: End-to-end retransmission
Stashing does no harm, except when buffering is reduced to 25% of the total
Uniform-random latency and throughput
Chart: Offered Load (flits/s/node)
| 0.01 | 0.108 | 0.20599999999999999 | 0.30399999999999999 | 0.40200000000000002 | 0.5 | 0.59799999999999998 | 0.69599999999999995 | 0.79400000000000004 | 0.89200000000000002 | 0.99
Baseline | 0.5975 | 0.60286 | 0.61005 | 0.6195 | 0.63215 | 0.6499 | 0.67674 | 0.72201 | 0.81479 | 1.1569 | 8.0276
Stash 100% Cap. | 0.5975 | 0.60286 | 0.61005 | 0.6195 | 0.63215 | 0.6499 | 0.67674 | 0.72201 | 0.81479 | 1.1569 | 7.9634
Stash 50% Cap. | 0.5975 | 0.60286 | 0.61005 | 0.6195 | 0.63215 | 0.6499 | 0.67674 | 0.72201 | 0.81479 | 1.158 | 7.1131
Stash 25% Cap. | 0.5975 | 0.60286 | 0.61005 | 0.6195 | 0.63215 | 0.6499 | 0.67674 | 0.72191 | 0.81759 | 7.2789 | 7.2789
Chart: Offered Load (flits/s/node)
| 0.01 | 0.108 | 0.20599999999999999 | 0.30399999999999999 | 0.40200000000000002 | 0.5 | 0.59799999999999998 | 0.69599999999999995 | 0.79400000000000004 | 0.89200000000000002 | 0.99
Baseline | 0.0099516 | 0.1076 | 0.2053 | 0.30299 | 0.40075 | 0.49858 | 0.59622 | 0.69368 | 0.79095 | 0.88697 | 0.88697
Stash 100% Cap. | 0.0099516 | 0.1076 | 0.2053 | 0.30299 | 0.40075 | 0.49858 | 0.59622 | 0.69368 | 0.79095 | 0.88697 | 0.88697
Stash 50% Cap. | 0.0099516 | 0.1076 | 0.2053 | 0.30299 | 0.40075 | 0.49858 | 0.59622 | 0.69368 | 0.79095 | 0.88696 | 0.88696
Stash 25% Cap. | 0.0099516 | 0.1076 | 0.2053 | 0.30299 | 0.40075 | 0.49858 | 0.59622 | 0.69367 | 0.79094 | 0.78583 | 0.78583
Notes: These are the classic latency/bandwidth curves for the four switch models using uniform-random traffic. The baseline in red is the best case. You can see that the stashing switches with full and 50% capacity perform as well as the baseline. It’s only the stashing switch with 25% capacity that suffers a bit in performance.

## Slide 24: Ecn transient absorption
Simulated pairs of applications:
Well-behaved “victim” injects at 40% bandwidth to many destinations
“Aggressor” injects at full bandwidth to a small number of destinations
Measured the performance of the victim only
Goal: determine if head-of-line blocking suffered by the victim is reduced
Goal: determine if the worst-case latency of the victim is reduced
Notes: Moving on to ECN. We simulated pairs of applications: a well-behaved victim that injects at 40% of maximum bandwidth to many destinations and an aggressor that injects at full bandwidth to a small number of destinations. As you would expect, the aggressor causes the congestion. We measured the performance of the victim only. Again we had two goals. First, to determine if stashing relieves the HoL blocking suffered by the victim and second, to determine if the worst-case latency suffered by the victim is reduced.

## Slide 25: Ecn transient absorption
Stashing almost completely eliminates excess victim latency
Aggressor starts
ECN succeeds
Notes: In this graph, I show the average latency of the victim over time. Let’s look at the baseline switch in red. At 20us, the aggressor starts running and congestion builds, causing the victim packets to experience higher latency. ECN starts almost immediately, but because it takes some time to take effect, congestion keeps building and the latency keeps increasing. At about 50us, ECN starts to reduce the congestion and then eliminates it by about 60us. The stashing switch, in green, diverts packets during the congestion event and you can see that it almost completely eliminates the HoL blocking caused by the aggressor. I also show that this effect is sensitive to the amount of stashing storage with the reduced-memory stashing switch shown in blue.

## Slide 26: Ecn transient tail latency
Stashing reduces the worst-case (tail) latency to just 3x the baseline without aggressor
Cumulative distribution of victim packet latencies
Notes: So stashing helps with the average latency, but what about the worst case? Here I show the inverse cumulative distribution of victim packet latencies. The further to the right a curve goes, the worse the latency and the higher a curve is, the more packets experience high latencies. So the best case is a tall skinny curve. That’s what you see for the yellow curve, which is the baseline switch running with no aggressor at all. In this case, the worst latency experienced by any packet is about 1.2us. The red curve is the baseline switch with the aggressor running. Here the worst case latency is literally off the chart and a large fraction of packets experience it. With stashing, in green, we get back to a fairly tight distribution where the worst-case latency of any packet is just 3 times that of the best case. This can have a significant effect on the victim application because entire collective operations can be stalled by a single unlucky packet. This chart also shows that there is sensitivity to the amount of stashing storage in blue.

## Slide 27: Conclusions
We believe that many interesting network capabilities are enabled by additional switch memory
Such as end-to-end retransmission and congestion mitigation
Stashing provides access to existing, unused switch memory via existing unused bandwidth
This initial evaluation indicates that stashing is worth further exploration
For details, please read the paper!
Notes: To conclude, we believe that many interesting network capabilities are enabled by additional memory. I showed you end-to-end retransmission and congestion mitigation as examples. I introduced stashing, which provides access to existing, unused switch memory via existing unused switch bandwidth. Finally, I presented results from our initial study that shows that stashing is worth further exploration.