## Slide 1: HPL and DGEMM Performance Variability on the Xeon Platinum 8160 Processor
John D. McCalpin, PhD
mccalpin@tacc.utexas.edu
Notes: This is less boring than it sounds!

## Slide 2: HPL and DGEMM Performance Variability due to Snoop Filter Conflicts on the Xeon Gold and Platinum 8160 Processors with 18, 20, 22, 24, 26, and 28 cores – and Xeon Phi x200 (KNL)
John D. McCalpin, PhD
mccalpin@tacc.utexas.edu
Notes: Detective story
New information
What next?

## Slide 3: The detective story (abridged)
Part 1
Notes: Very abridged – please read paper!

## Slide 4: Context: late October 2017
During bringup and acceptance of the 1736-node SKX partition of TACC’s Stampede2 system, the team noticed:
  A small fraction of single-node HPL runs delivered significantly lower performance than expected – performance drops of >10%
  All large multi-node runs showed some slow nodes
    Static load distribution causes this to slow down the entire run
  The problem did not appear to be limited to any particular subset of nodes
After ruling out hardware problems (e.g., throttling due to bad power supplies), I was asked to investigate…
Notes: Reproduce, simplify, test, etc…

## Slide 5: “long hours of good, old-fashioned investigative work”
Part 1a
Notes: Finding the root cause.

## Slide 6
Sorted single-node HPL performance
392 nodes x 7 runs
Performance rescaled by per-node median
Compacts 13% range in node median values
About 11 of the 2744 runs (0.4%) were more than 10% slower than the node’s median
10 different nodes
Notes: Execution time only – no performance counters yet.
>500 nodes tested but only 392 nodes had the 7 runs needed to compute medians.
Dozens of different nodes showed >=5% slowdowns.

## Slide 7
Single Node HPL execution time vs DRAM Read Traffic
392 nodes x 3 runs
Surprisingly high variability in DRAM traffic for the “good” runs….
The 10 slowest runs all had elevated DRAM traffic.
Notes: If you are Dr. Bandwidth, you always measure memory traffic.
Read memory controller performance counters before/after each execution.
Next simplify workload and test on dedicated nodes.

## Slide 8: Simplified Workload: 2s HPL  1s DGEMM
Run on 31 dedicated nodes, socket 0 only
Many sets of runs, varying many parameters
Typically >20 executions on each node to get enough runs to see several instances of rare (1 in 100) events
Many different groups of programmable core hardware performance counter events
  31 distinct counter events tested
  Some events ruled out possible mechanisms
KEY OBSERVATION: slow runs were slow for the duration – no matter how many DGEMM calls were made in the run
Notes: Decouple sockets, shorten runtime, simplify structure.
Performance counter infrastructure at github.
Over 25,000 DGEMM runs in total, over 240 GB of performance counter output.

## Slide 9
DGEMM
Different vendor
Different benchmark
Single socket
31 nodes x 105 runs
L2 fills vs run time:
Surprisingly high variation in L2 fills across “good” runs….
Weak “global” correlation, but strong correlation with performance outliers
Dotted line is 1 ns per “extra” L2 fill – consistent with plausible concurrency
Notes: L2 fills rather than L2 stalls, but pattern is similar.
Next look at core-by-core values for good and “slow” runs.

## Slide 10
L2 Fills by Core for two consecutive DGEMM runs on the same socket
“Good” trial is at or above median performance
Total L2 fills at high end of “normal” range
Only 5 cores showed close to the minimum observed average L2 Fill count – most were about 50% higher
Notes: One of 15-20 cases reviewed (mostly different nodes, with different perf counter events)
Different sets of cores had high counts in each run (even on same node)
L2 caches are private and 2MiB pages fully control L2 cache index bits.
Something external must be causing the L2 misses?

## Slide 11
L2 Fills by Core for two consecutive DGEMM runs on the same socket
“Slow” trial:
+47% L2 fills
-38% GFLOPS
1.6x execution time
+44% DRAM Reads
Note:
3 cores matched minimum L2 Fills
These cores showed higher average frequencies
Cores 6, 9, 19 were in spin-wait long enough to switch to non-AVX512 frequencies
Notes: One of 15-20 cases reviewed (mostly different nodes, with different perf counter events)
Different sets of cores had high counts in each run (even on same node)
L2 caches are private and 2MiB pages fully control L2 cache index bits.
What could be causing the L2 misses?

## Slide 12: A suspect: the “Snoop Filter”
Previous Intel processors used an inclusive L3 cache to track lines held in L1 and L2 caches
  Nehalem/Westmere, Sandy Bridge/Ivy Bridge, Haswell/Broadwell
In “Skylake Xeon” the L3 cache is NOT inclusive
  The cache tracking functionality is still required
  Performed by inclusive “Snoop Filter” rather than by L3 cache
  Almost completely undocumented, but things can be learned….
Experience with similar designs was essential
  “Sparse directory” used in the SGI Origin 3000
  “HyperTransport Assist” in AMD “Istanbul” and later processors
Notes: Snoop Filter is similar to directory of inclusive L3, but without room to store the data for the cache lines.
Key is inclusivity – lines tracked by an entry must be invalidated before that entry can be freed.

## Slide 13: Snoop Filter properties
Like the L3, the Snoop Filter is distributed, with addresses mapped to Snoop Filter entries by an undocumented hash
Snoop Filter is a cache, tracking lines most recently loaded into cores’ L1/L2 caches
  New entries replace old entries – forcing lines tracked by old entry to be invalidated in all L1/L2 caches
Hypothesis: “Bad” combinations of physical addresses interact with the hash to overload some Snoop Filter sets
  Causes “live” data to be evicted, and allows “private” caches to interfere with each other!
Notes: Is the Snoop Filter the primary source of the problems I am seeing? Yes.
I added CHA counters to measure Snoop Filter Evictions and ran another ensemble.

## Slide 14
DGEMM
31 nodes, 103 runs each
(“Excess” is relative to the minimum count across the 3179 runs in the ensemble)
All slow runs have
High L2 fills
Notes: About 1% of the runs are more than 10% slower than the fastest run.

## Slide 15
DGEMM
31 nodes, 103 runs each
(“Excess” is relative to the minimum count across the 3179 runs in the ensemble)
All slow runs have
High L2 fills
Snoop Filter Evictions of the same magnitude as the excess L2 fills
Notes: SF Evictions clearly account for most excess L2 fills.
But there is 1 more thing….

## Slide 16
DGEMM
31 nodes, 103 runs each
(“Excess” is relative to the minimum count across the 3179 runs in the ensemble)
All slow runs have
High L2 fills
Snoop Filter Evictions of the same magnitude as the excess L2 fills
Elevated DRAM Reads (much higher latency per operation than L2 fills from L3)
Notes: There is a lot of interesting detail in the results at around 110 seconds – too much for today.
For the slower runs, it looks like a fraction of the lines evicted by SF evictions conflict in the L3, and so must be retrieved from DRAM.

## Slide 17: Mitigation for dgemm and hpl
Part 1b
Notes: Based on industry experience, I wondered if contiguous physical addresses might fix this problem?

## Slide 18
Baseline: 1s DGEMM
Notes: Baseline with 2MiB pages

## Slide 19
Repeat with 1 GiB pages
Notes: Tail almost disappears in both width and depth.

## Slide 20
Detail of slowest 10% of trials
Notes: So what about HPL?
Intel provided a test version in December 2017

## Slide 21
Single Node HPL on 1GiB pages
31 nodes x 247 runs
The error bars show the full range of minimum, average, maximum GFLOPS across the 247 runs on each node
Largest max/min range is 0.7%
Fastest node is 8.6% faster than slowest node
Notes: This is amazingly tight performance repeatability.
The range of average performance increases with cluster size, exceeding 12% for our full 1736-node SKX partition.

## Slide 22: Full-System HPL Performance
4200 Xeon Phi 7250 + 1736 dual Xeon Platinum 8160
November 2017: 8.318 PFLOPS
June 2018: 10.681 PFLOPS  +28.4%
More than ½ of the improvement is from using 1 GiB pages on the SKX nodes to prevent Snoop Filter Conflicts
Additional boost from static load balancing
  KNL – three performance bins
  SKX – six performance bins
Eliminating most performance variability allowed us to jump to a much larger problem size
Notes: Intel provided a full HPL version in March 2018 and we ran in April 2018
These are ballpark estimates – it would be a huge project to measure the details at this scale.
”Practical Peak Performance” 8.77 PF on KNLs + 3.73 PF on SKX = 12.5  10.68 = 85% peak

## Slide 23: New measurements and analyses
Part 2
Notes: Simplification to array summation kernel allowed quick testing on other systems
(this is mostly new material, not in the paper)

## Slide 24: Another simplification: Repeated Array Summation
Single-socket DGEMM was a shorter test than HPL, but it still takes ~100 seconds per trial, and is closed source
If the problem is that Snoop Filter Conflicts are evicting data from the L2, then repeatedly reading a large, L2-containable array should show the signal even more clearly
  This works! Under 1s per trial.
  All L2 misses are due to Snoop Filter Conflicts
Two versions are in the SKX-SF-Conflicts github repo
  Array starting at explicit offsets within 1 GiB pages
  Array mapped to 2 MiB huge pages
Notes: This lets me more directly address my hypothesis about a lack of conflicts for contiguous physical addresses

## Slide 25
Chart: Offset of Center of 22.9 MiB block above base of 1GiB page
No Snoop Filter Conflicts in the first 32 MiB of each 256MiB
32 MiB > L2 cache
But: 32 MiB is smaller than L2+L3 (57 MiB)
Snoop Filter Evictions for contiguous physical addresses (1G pages)
Notes: I was wrong, conflicts can be bad.
Pattern repeats every 256 MiB
If reused space is in 1st 32 MiB, no SF conflicts

## Slide 26
Chart: 
Chart: 
Chart: 
Chart: 
24c
Only these 4 core counts show Snoop Filter Conflicts for contiguous physical addresses
18c
20c
KNL
Notes: These 4 core counts have both the systematic and random issues.
The random component probably comes from needing to map more 2MiB pages than the associativity of the snoop filter.

## Slide 27
Chart: 
| 14c | 16c | 18c | 20c | 22c | 24c | 26c | 28c | KNL
10% probability | 0 | 0 | 0.046 | 0.049 | 0.015 | 0.11 | 0.012 | 0.012 | 0.099
1% probability | 0 | 0 | 0.183 | 0.184 | 0.057 | 0.29 | 0.058 | 0.068 | 0.301
0.1% probability | 0.004 | 0 | 0.351 | 0.392 | 0.131 | 0.434 | 0.122 | 0.157 | 0.506
Average Snoop Filter Eviction Ratio for repeated array read test on 2 MiB pages
Tests run on:
14c Xeon Gold 6132
16c Xeon Gold 6142
18c Xeon Gold 6150
20c Xeon Gold 6148
22c Xeon Gold 6152
24c Xeon Platinum 8160
26c Xeon Platinum 8170
28c Xeon Platinum 8180
KNL Xeon Phi 7250
Thanks: Dell Customer Solutions Center!
Notes: These are *average* miss rates -- individual cores can have higher miss rates.
Details are interesting, but not for today.

## Slide 28: implications
Part 3

## Slide 29
Workload Implications (1)
Snoop Filter Conflicts are expected to impact jobs with:
  High L2/L3 cache re-use, AND
  High L2/L3 access rate, AND
  Large L2/L3 “footprint” (>10 MiB), AND
  Static load distribution with synchronization
Each of these properties is individually fairly common – the combination of all four is hard to estimate
Currently collecting performance counter data across all jobs to look for occurrence in “real” applications….
Notes: 1. The uncertainty is probably more damaging than the performance loss.
2. Needles and haystacks, perhaps easier to look for codes with these properties

## Slide 30
Workload Implications (2)
Examples:
  If an application benefits from cache-blocking, it satisfies the first two criteria (high hit rate and high access rate), and typically the third (large footprint)
  If an application is expected to be fully cache-contained, it might not be?
    Impact is easy to demonstrate with simple codes
What about something like autotuning?
  If the tuning run experiences conflicts, the poor tuning choices will persist
Notes: Cache-contained shallow water model, cache-contained FFTs
What about mitigations?

## Slide 31
Specific Mitigations
For DGEMM: upgrade MKL to Intel 2018 update 3 or 2019
  New implementation does not generate Snoop Filter conflicts
  Does not fix the problem, but does avoid it
In some cases, conflicts can be eliminated with 1 GiB pages
  Not easy to use
  1 GiB pages must be pre-allocated
  Reboot may be required to allocate and/or deallocate
  Use on stack & heap requires LD_PRELOAD to link libhugetlbfs
Notes: The new DGEMM implementation is not magic, but certainly no time to discuss today

## Slide 32
General Mitigations? (1)
If the address hash formula was known, conflicts for groups of 2 MiB pages could be predicted in advance
  This could be used to create a routine to sort the free page list(s) to minimize conflicts for groups of ~10-30 2 MiB pages
    E.g., zonesort on our KNL systems in MCDRAM Cache mode
  The address hash is currently “Intel top secret”
Can Intel develop approximations that will avoid conflicts without releasing confidential information?
  Almost certainly yes, but….
  May require a larger level of pressure than one customer can apply….
Notes: Now able to predict some conflicts on 24c processors.
Not yet production-ready.

## Slide 33
General Mitigations? (2)
Maybe a machine learning approach could predict conflicts?
  Behavior is deterministic, but depends on unknown properties of unknown operations on high-order physical address bits
  Input is unordered
  Highly nonlinear – no detectable conflicts until a set overflows, then all allocations to that set will conflict
  I would be happy to receive advice from experts in this area….
Notes: Now able to predict some conflicts on 24c processors.
Not yet production-ready.

## Slide 34
Summary
Infrequent, but significant, performance reductions were seen on 24-core Xeon Platinum 8160 processors when running the HPL benchmark (both single-node & multi-node)
Systematic testing eventually led to identification of the root cause – conflicts in the Snoop Filter due to “bad” combinations of physical addresses
Applies to all Intel Xeon Scalable processors with ≥18 cores
Specific mitigations have been found for HPL and DGEMM
General software mitigations do not yet exist
  If this is important to you, make sure your Intel representative knows
Notes: Intel has prepared a response, but I don’t know when it will be released – go ask them!

## Slide 35: Software Reproducibility Resources
https://github.com/jdmccalpin/periodic-performance-counters
  SKX-specific program to read all core and uncore performance counters in the background at a specified interval
  Low-overhead global monitoring: ~1% of one logical processor at 1s interval
https://github.com/jdmccalpin/simple-MKL-DGEMM-test
  Simple driver to call Intel MKL DGEMM a specified number of times, reporting timing and performance data
  Supports 4KiB, 2MiB, 1GiB pages
  Includes scripts to run and analyze ensembles of runs
https://github.com/jdmccalpin/SKX-SF-Conflicts
  Reads (sums) a contiguous (virtual) array 1000 times with built-in Core and Uncore performance counter support for SKX
  Supports 4KiB, 2MiB, 1GiB pages
  Includes scripts to run and analyze ensembles of runs
Notes: These are the primary resources described in the “Artifacts Description Appendix” of the paper.

## Slide 36: Appendix: performance counters
https://github.com/jdmccalpin/periodic-performance-counters
Uses a single thread to read all core and uncore performance counters at a specified interval (default 1 second)
  96 logical processors * (3 fixed counters + 4 programmable counters)
  48 CHAs * 4 programmable counters
  12 DRAM channels * (1 fixed counter + 4 programmable counters)
  Socket-level RAPL, IO, PCU counters
  >900 counters per sample, >50KiB text output per sample
Low-overhead: ~1% of one logical processor at 1 second intervals
Data held in memory until job completion (or 10,000 samples acquired)
  Text output is Lua (& Python?) compatible assignment statements
Testing generated >240 GiB of performance counter data
Notes: Measure everything to allow later re-analysis.

## Slide 37: For more information: www.tacc.utexas.edu
John D. McCalpin, PhD
mccalpin@tacc.utexas.edu
512-232-3754